Dual Porosity Modeling and Multi-scale Finxite Volume Methods

---
Motivation
Challenges:
heterogeneous parameters on multiple scales
strongly discontinuous material properties, e.g. K spans multiple length scales and has multiscale structure
→ all scales impact flow behaviour
high-resolution of all details computationally not possible
[Speaker Notes: high-permeable fractures embedded in a low-permeable matrix Need for alternative modelling approaches, that reduce complexity of system but are able to reproduce important processes]

---
Modeling Flow in Fractured Porous Media
   Common modeling approaches
Continuum approaches
Discrete approaches
Multi-scale methods
[Speaker Notes: high complexity and variety of problems: not feasible to describe system in great detail , and development of a generally applicable model is difficult different modeling approaches and numerical methods have been developed for certain types of problems on dertain scales]

---
Modeling Flow in Fractured Porous Media
Common modeling approaches
Continuum approaches
upscaled representation of geometries and parameters
→ efficient
→ determination of effective parameters and exchange
    functions not straightforward
Discrete Approaches
Multi-scale methods

---
Modeling Flow in Fractured Porous Media
Common modeling approaches
Continuum approaches
Discrete approaches
explicit resolution of fractures in the domain
→ accurate
→ applicability limited to smaller scales (extensive data
    requirement, huge systems)
Multi-scale methods
fracture network
EDFM
DFM
[Speaker Notes: discrete fracture models (DFM) : fractures are discretely represented in the grid. that way, location and geometry of individual fractures is explicitly accounted for. In classic DFM, it is assumed that the fracture length is considerably larger than the fracture width -> fractures are discretized using lower-dimensional elements. Conforming matrix and fracture mesh, i.e. fracture cells are restricted to align with interfaces of matrix cells -> complex unstructured gridding techniques required. often, many small and ill-shaped elements at intersections -> huge degrees of freedom, and time-step restrictions alternative: Embedded discrete fracture models: independent grids for fractures and matrix. that way, expensive generation of conforming mesh is avoided. Transfer between matrix and fracture, which was calculated directly in the DFM, is now approximated by a well-like transfer function.]

---
Modeling Flow in Fractured Porous Media
Common modeling approaches
Continuum approaches
Discrete approaches
Multi-scale methods
resolve fine-scale data, but solve coarse-scale system

---
Hierarchical Fracture Modeling (HFM)
Discre

---
Dual-Porosity Model
Discre

---
The Multi-Scale Restricted Smooth Basis
Method for Fractured Porous Media (F-MsRSB)
Discre